Cheese Board: Cheddar Instructions

Date:	24/09/17	Version:	1.0	By:	Matt Little

This is an ESP8266 breakout board with small display, user inputs and WS2812 LEDs. / This is designed as a low cost platform to quickly get started with projects with the ESP8266. We wanted to design something that got you up and running with your project idea quickly and easily. / The main processor is based upon the ESP8266 system-on-chip from Espressif Systems. / This can be programmed via the Arduino IDE (or your favourite IDE). / This is a reasonably simple kit which requires some soldering. / It should take 1-2 hours to build. / Not suitable for under 12 years old.

# Parts included:

			Laser-cut Enclosure			3 x AA rechargeable batteries
1W Solar PV Modules

								Battery Holder

DC-DC / Converter
								7 x M3 Hex spacers

PCB								7 x M3 6mm / 7 x M3 8mm

								Sticky Pads
Wire
		Diode 1N4001				Switch + 2 x M2.5 screws

# Enclosure Parts:
Top 1		Front
Top 2
Top 3		Back

Bottom 1
Bottom 1
Bottom 1		Switch / Holder

# Parts list:
Item	Ref	Quantity
Capacitors. 100nf / U1 NODEMCU / R1 330 / SW1 ON/OFF / U2 74LVC1G17 / PCB / NODE MCU 15 way connector / OLED 4 way connector / OLED Fittings / Enclosure	C1-5	5
Diode. 1N5819	D1, D2	2
LED. WS2812. Pre soldered	D3-7	5
LED. Red. NOT included	B8	Not Included
Display. OLED. 0.96"	DISP1	1
Encoder	ENC1	1
Fuse. 500MA	F1	1
NodeMCU
USB micro Socket. Pre-soldered	P1	1
2 way screw terminal. 5V	P2	1
HC-11 Serial. Optional	P3
Software Serial. Optional	P4
Node MCU header. 15 way.	P5, P6	2
PCB		1
Switch		1
M2 Machine screws 10m long		2
M3 Machine screws 6mm long		7
M3 Machine screws 8mm long		7
M3 Threaded Hex spacers 8mm long		7
3 x AA Battery Holder		1
AA NiMH Rechargable Batteries		3
1Wp Solar PV Units. 5V max out.		2
Wire – Red and Black		length
Laser-cut enclosure (9 pieces) 3mm Ply		1
Double sided sticky pads		3

# Tools required:

		Long-nosed / Pliers
Soldering Iron		Posi-drive / Screwdriver
Solder
Side cutters

Instructions:
Step: 1	Solder capacitors

Step: 2	Solder diodes

Step: 3	Solder switch

Step: 4	Solder header pins

Step: 5	Solder encoder

Step: 6	Solder fuse

Step: 7	Solder screw terminals (if needed)

Step: 8	Fit LCD

Step: 9	Add enclosure

Step: 10	Build is finished!
Test with micro-USB cable. / Switch on and check LEDs light.		Have a nice cup of tea.

Step: 11	Upload software

# Contact details:
This kit has been designed and produced by:

The Curious Electric Company
hello@curiouselectric.co.uk
www.curiouselectric.co.uk
Hopkinson Gallery, 21 Station Street, Nottingham, UK, NG2 3AJ

We would like you to be happy with this kit. If you are not happy for any reason then please contact us and we will help to sort it out.

Please email hello@curiouselectric.co.uk with any questions or comments.
Please tweet us at @curiouselectric

If any parts are missing from your kit then please email hello@curiouselectric.co.uk with details, including when and where the kit was purchased.

More technical information can be found via www.curiouselectric.co.uk

# Circuit Schematic:

# PCB Design:
# Useful Information:

0

1

2

3

4

5

6

7

8

9